Specification clauses

To be read with Preliminaries/General conditions

Open mesh steel panel high security fencing/gates

CLD Securus SR1 358 Rigid Mesh Panel System.

• Height:	2440mm/3000mm * delete as required

• Nominal height: 	2.4m/3.0m * delete as required

• Mesh & wire: 	76.2 x 12.5 mm mesh; 4 mm wire, high aluminium content galvanised and polyester powder-coated to minimum 80 microns

• Posts: 	80 x 60 mm special flanged section, galvanised after manufacture and polyester powder-coated with 120 x 6mm full length clamp bar galvanised and polyester powder-coated to match fencing

• Corner Posts: 	80 x 80 mm SHS, galvanised after manufacture and polyester powder-coated to match fencing.

• Fixings: 		M8 cup square bolt with permacone nut, stainless steel.

• Set posts: 	Set posts in holes 300 mm diameter x 800** mm deep, filled not less than half the depth with concrete, as clause 620.

• Maximum post centers: 	2520mm

• Bottom of fencing to be: 	approx. 50 mm above final ground level. * delete as required

300mm Ground Bury. * delete as required

• Other requirements: 	PPC Colour Green RAL 6005. A full range of RAL Colours are available including marine grade and metallics.

• System conforms to:	LPS1175 SR1

Secured by Design

‘Approved for Government Use’

** Depending on fence height

NOTES: 	Additional security features apply to product that are not included in specification for security reasons.

All dimensions are nominal, for further information please contact Farm Relief Fencing. All information is correct at time of production. We reserve the right to alter specification without notice.