Specification clauses

To be read with Preliminaries/General conditions

Open mesh steel panel decorative fencing/gates

CLD ScreenFence Double Wire Rigid Mesh Panel System.

• Height:	1230mm/1830mm/2030mm/2430mm (other heights are available on request) * delete as required

• Nominal height: 	1.2m/1.8m/2.0m/2.4m (other heights are available on request) * delete as required

• Mesh & wire: 	200 x 50mm mesh; 6mm verticals and twin 8mm horizontal nominal wires, galvanised and polyester powder-coated to 60 microns. * delete as required.

200 x 50mm mesh; 5mm verticals and twin 6mm horizontal nominal wires, galvanised and polyester powder-coated to 60 microns. * delete as required.

• ScreenFence Weave: 	Full Panel Weave/Partial Weave (increments of 200mm) * delete as required

• Posts: 	60 x 40 mm to 120 x 60mm RHS, hot dip galvanised and polyester powder-coated with 40 x 5 mm full length clamp bar, galvanised and polyester powder-coated to match fencing.

• Fixings: 	M8 x 40 mm stainless steel pin-hex dome head security bolt.

• Set posts: 	Set posts in holes 450 mm diameter x 1000** mm deep, filled not less than half the depth with concrete, as clause 620.

• Maximum post centers: 	2520mm

• Other requirements: 	A full range of RAL Colours are available marine grade and metallics.

A full range of ScreenFence Weaves are available.

• Sheardrive™ fixing if required instead of pin hex.

** Depending on fence height and ground conditions

NOTES: 	All dimensions are nominal, for further information please contact Farm Relief Fencing. All information is correct at time of production. We reserve the right to alter specification without notice.