Specification clauses

To be read with Preliminaries/General conditions

Open mesh steel panel perimeter security fencing/gates

CLD Dulok Double Wire Rigid Mesh Panel System.

• Height:		630mm/830mm/1030mm/1230mm/1430mm/1630mm/1830mm/2030mm/

2430mm/2660mm/2860mm/3030mm/3460mm/3860mm/4060mm/4460mm/

4860mm/5060mm/5460mm/5660mm/6060mm* delete as required

• Nominal height: 	0.6m/0.8m/1.0m/1.2m/1.4m/1.6m/1.8m/2.0m/2.4m/2.7m/2.8m/3.0m/

3.4m/3.8m/4.0m/4.4m/4.8m/5.0m/5.4m/5.6m/6.0m* delete as required

• Mesh & wire: 	200 x 50mm mesh; 6mm verticals and twin 8mm horizontal nominal wires, galvanised and polyester powder-coated to 60 microns. * delete as required

200 x 50mm mesh; 5mm verticals and twin 6mm horizontal nominal wires, galvanised and polyester powder-coated to 60 microns. * delete as required

• Posts: 	60 x 40 mm RHS, galvanised after manufacture and polyester powder-coated with 40 x 5mm full length clamp bar galvanised and polyester powder-coated to match fencing. (630mm – 2430mm Panels ONLY) * delete as required

80 x 40 mm RHS, galvanised after manufacture and polyester powder-coated with 40 x 5mm full length clamp bar galvanised and polyester powder-coated to match fencing. (2860mm – 4060mm Panels ONLY) * delete as required

100 x 50 mm RHS, galvanised after manufacture and polyester powder-coated with 40 x 5mm full length clamp bar galvanised and polyester powder-coated to match fencing. (4460mm – 5460mm Panels ONLY) * delete as required

120 x 60 mm RHS, galvanised after manufacture and polyester powder-coated with 40 x 5mm full length clamp bar galvanised and polyester powder-coated to match fencing. (5560mm – 6060mm Panels ONLY) * delete as required

• Fixings: 		M8 x 40 mm stainless steel pin hex dome-head security screws.

• Set posts: 	Set posts in holes 300 mm diameter x 800** mm deep, filled not less than half the depth with concrete, as clause 620.

• Maximum post centers: 	2520mm

• Bottom of fencing to be: 	approx. 50 mm above final ground level.

• Other requirements: 	PPC Colour Green RAL 6005. A full range of RAL Colours are available including marine grade and metallics.

• Sheardrive™ fixing if required instead of pin hex.

** Depending on fence height

NOTES: 	Fence heights above 3030mm are made up of 2 or more panels

All dimensions are nominal, for further information please contact Farm Relief Fencing. All information is correct at time of production. We reserve the right to alter specification without notice.