Specification clauses

To be read with Preliminaries/General conditions

Open mesh steel panel general purpose fencing/gates

CLD Dulok-8 SR1 Double Wire Rigid Mesh Panel System.

• Height:		1830mm/2030mm/2430mm/3030mm/* delete as required

• Nominal height: 	1.8m/2.0m/2.4m/3.0m/* delete as required

• Mesh & wire: 	200 x 50mm mesh; 6mm verticals and twin 8mm horizontal nominal wires, galvanised and polyester powder-coated to 60 microns.

• Posts: 	60 x 40 mm RHS, galvanised and polyester powder-coated with 40 x 5mm full length clamp bar galvanised and polyester powder-coated to match fencing. (1830mm – 2430mm Panels ONLY) * delete as required

80 x 40 mm RHS, galvanised and polyester powder-coated with 40 x 5mm full length clamp bar galvanised and polyester powder-coated to match fencing. (3030mm Panels ONLY) * delete as required

• Fixings: 		M8 x 40 mm stainless steel CLD Sheardrive Fixings

• Set posts: 	Set posts in holes 300 mm diameter x 800** mm deep, filled not less than half the depth with concrete, as clause 620.

• Maximum post centers: 	2520mm

• Bottom of fencing to be: 	approx. 50 mm above final ground level.

• Other requirements: 	PPC Colour Green RAL 6005. A full range of RAL Colours are available including marine grade and metallics.

• System conforms to:		LPS1175 SR1

Secured by Design

** Depending on fence height

NOTES: 	Additional security features apply to product that are not included in specification for security reasons.

All dimensions are nominal, for further information please contact Farm Relief Fencing. All information is correct at time of production. We reserve the right to alter specification without notice.