Specification clauses

To be read with Preliminaries/General conditions

Open mesh steel panel high security fencing/gates

CLD Ultimate Extra SR1 Profiled Panel System.

• Height:		2030mm/2430mm/3030mm* delete as required

• Nominal height: 	2.0m/2.4m/3.0* delete as required

• Mesh & wire: 	165 x 25mm mesh; 6 mm nominal wire with 4 profiles, galvanised and polyester powder-coated to 60 microns.

• Posts: 	80 x 40 mm RHS, galvanised after manufacture and polyester powder-coated with 41 x 21mm clamping channel galvanised and polyester powder-coated to match fencing.

• Fixings: 		CLD ‘SafeTFix’ Hidden Fixing System

• Set posts: 	Set posts in holes 300 mm diameter x 800** mm deep, filled not less than half the depth with concrete, as clause 620.

• Maximum post centers: 	2485mm (2030mm – 2430mm ONLY)* delete as required

2060mm (3030mm ONLY)* delete as required

• Bottom of fencing to be: 	approx. 50 mm above final ground level.

• Other requirements: 	PPC Colour Green RAL 6005. A full range of RAL Colours are available including marine grade and metallics.

• System conforms to:	LPS1175 SR1

Secured by Design

** Depending on fence height

NOTES: 	Additional security features apply to product that are not included in specification for security reasons.

All dimensions are nominal, for further information please contact Farm Relief Fencing. All information is correct at time of production. We reserve the right to alter specification without notice.