Specification clauses

To be read with Preliminaries/General conditions

Open steel panel sport fencing/gates

CLD Ball Stop Netting System.

• Height:	500mm – 10000mm

• Nominal height: 	0.5m – 10.0m

• Ball Stop Netting: 	25 x 25mm/50 x 50mm/100 x 100mm/120 x 120mm in a range of mesh densities

• Posts: 	RHS or SHS depending upon application

• Fixings: 		Depending on application

• Set posts: 	Set posts in holes 300 mm diameter x 800** mm deep, filled not less than half the depth with concrete, as clause 620.

• Maximum post centers: 	Depending on application

• Bottom of fencing to be: 	approx. of 50 mm above final ground level.

• Other requirements: 	Please contact CLD Fencing Systems for full updated colour chart, whilst every effort will be made to match to a RAL colour there may be chromatic differences

** Depending on fence height

NOTES: 	All dimensions are nominal, for further information please contact Farm Relief Fencing. All information is correct at time of production. We reserve the right to alter specification without notice.