Specification clauses

To be read with Preliminaries/General conditions

Open mesh steel panel double wire temporary fencing

CLD FenceSafe Dulok-Lite Temporary Fencing System.

• Height: 	1830/2030/2430mm*

• Nominal height: 	1.8/2.0/2.4m*

• Mesh:	CLD Dulok-Lite Double Wire Panel System Mesh & wire: 200 x 50mm mesh; two 6mm horizontal wires; one 5mm vertical wire, galvanised and polyester powder-coated to 60 microns.

Panels to be manufactured to BS1722 Part 14.

• Posts: 				60 x 60mm RHS mounted on CLD FenceSafe base, galvanised

after manufacture and polyester powder-coated with 47 x 25 mm steel clips galvanised and polyester powder-coated to match fencing.

• Fixings: 				M8 x 40 pin hex dome head security screws.

• Maximum post centers: 		2.5/1.25m*

• Set posts: 	CLD FenceSafe base unit, with 4-way adjustable bracket and 200kg of ballast. System to be designed in accordance to BS6399-2 or BS EN 1991 for area of use.

• Bottom of fencing to be: 		approx.	50mm above final ground level.

• Other requirements: 	PPC Colour Black RAL 9005/Green 6005* (other RAL Colours Available).

*Delete as required

For further information please contact Farm Relief Fencing.