Specification clauses

To be read with Preliminaries/General conditions

Open mesh steel panel security temporary fencing

CLD Securus Lite Temporary Fencing System.

• Height: 	1800/2000/2400mm*

• Nominal height:	1.8/2.0/2.4m*

• Mesh: 	CLD Securus-Lite Rigid Panel System 76.2 x 12.5mm mesh; 4 mm wire, high aluminium content galvanised and polyester powder-coated to minimum 80 microns.

Panels to be manufactured to BS1722 Part 14.

• Posts: 				60 x 60mm SHS mounted on CLD FenceSafe base, galvanised

after manufacture and polyester powder-coated to match fencing and clamp bar.

• Fixings: 				CLD ‘SafeTFix’ Hidden Fixing System.

• Maximum post centers: 		2.5/1.25m*

• Set posts: 	CLD FenceSafe base unit, with 4-way adjustable bracket and 200kg of ballast. System to be designed in accordance to BS6399-2 or BS EN 1991 for area of use.

• Bottom of fencing to be: 		approx.	50mm above final ground level.

• Other requirements: 	PPC Colour Black RAL 9005/Green 6005* (other RAL Colours Available).

*Delete as required

For further information please contact Farm Relief Fencing.