Specification clauses

To be read with Preliminaries/General conditions

Open mesh steel panel sports fencing/gates

CLD Dulok Rebound Double Wire Rigid Mesh Panel System.

• Height:	2.0m Full Rebound/3.0m with Rebound to 1.2m as combination panel (other heights and combinations are available using Dulok Sports or Dulok Rebound Panels as a double lift) * delete as required

• Nominal height: 	2.0m/3.0m/4.0m/4.5m/5.0m/6.0m (other heights and combinations are available using Dulok Sports or Dulok Rebound Panels as a double lift) * delete as required

• Mesh & wire: 	50 x 66.5mm rebound mesh; 6mm verticals and twin 8mm horizontal nominal wires, galvanised and polyester powder-coated to 60 microns. * delete as required

50 x 66.5mm rebound detail to 1.2m then 200 x 50mm mesh; 6mm verticals and twin 8mm horizontal nominal wires, galvanised and polyester powder-coated to 60 microns. * delete as required

• Posts: 	80 x 40 mm RHS, galvanised after manufacture and polyester powder-coated with 40 x 5mm full length clamp bar galvanised and polyester powder-coated to match fencing.

• Fixings: 	M8 x 40 mm stainless steel pin hex dome-head security screws.

• Set posts: 	Set posts in holes 300 mm diameter x 800** mm deep, filled not less than half the depth with concrete, as clause 620.

• Maximum post centers: 	2520mm

• Bottom of fencing to be: 	approx. 50 mm above final ground level.

• Other requirements: 	PPC Colour Green RAL 6005. A full range of RAL Colours are available from CLD Fencing Systems including marine grade and metallics.

• Sheardrive™ fixing if required instead of pin hex.

** Depending on fence height

NOTES: 	Fence heights above 3030mm are made up of 2 or more panels

All dimensions are nominal, for further information please contact Farm Relief Fencing. All information is correct at time of production. We reserve the right to alter specification without notice.