Specification clauses

To be read with Preliminaries/General conditions

Open mesh steel panel general purpose fencing/gates

CLD Dulok-Lite Double Wire Rigid Mesh Panel System.

• Height:		630mm/830mm/1030mm/1230mm/1430mm/1630mm/1830mm/2030mm/

2430mm/2660mm/2860mm/3030mm/3460mm/3860mm/4060mm*

delete as required

• Nominal height: 	0.6m/0.8m/1.0m/1.2m/1.4m/1.6m/1.8m/2.0m/2.4m/2.7m/2.8m/3.0m/

3.4m/3.8m/4.0m* delete as required

• Mesh & wire: 	200 x 50mm mesh; 5mm verticals and twin 6mm horizontal nominal wires, galvanised and polyester powder-coated to 60 microns.

• Posts: 	60 x 40 mm RHS, galvanised after manufacture and polyester powder-coated with 47 x 35 mm steel clips galvanised and polyester powder-coated to match fencing. (630mm – 2430mm Panels ONLY) * delete as required

80 x 40 mm RHS, galvanised after manufacture and polyester powder-coated with 47 x 35 mm steel clips galvanised and polyester powder-coated to match fencing. (2860mm – 4060mm Panels ONLY) * delete as required

• Fixings: 		M8 x 40 mm stainless steel pin hex dome-head security screws.

• Set posts: 	Set posts in holes 300 mm diameter x 800** mm deep, filled not less than half the depth with concrete, as clause 620.

• Maximum post centers: 	2520mm

• Bottom of fencing to be: 	approx. 50 mm above final ground level.

• Other requirements: 	PPC Colour Green RAL 6005. A full range of RAL Colours are available including marine grade and metallics.

• Sheardrive™ fixing if required instead of pin hex.

** Depending on fence height

NOTES: 	All dimensions are nominal, for further information please contact Farm Relief Fencing. All information is correct at time of production. We reserve the right to alter specification without notice.