Specification clauses

To be read with Preliminaries/General conditions

Open mesh steel panel perimeter security fencing/gates

CLD Multiplus Profiled Variable Rigid Mesh Panel System.

• Height:		1800mm/2000mm/2400mm/3000mm* delete as required

• Nominal height: 	1.8m/2.0m/2.4m/3.0m* delete as required

• Mesh & wire: 	200 x 45mm (200 x 25mm Variable) mesh; 4mm vertical and 6mm horizontal nominal wire with 3 profiles, galvanised and polyester powder-coated to 60 microns.

• Posts: 	60 x 40 mm RHS, galvanised after manufacture and polyester powder-coated with 47 x 25 mm steel clips galvanised and polyester powder-coated to match fencing. (1800 – 2400mm Panels ONLY) * delete as required

80 x 40 mm RHS, galvanised after manufacture and polyester powder-coated with 47 x 25 mm steel clips galvanised and polyester powder-coated to match fencing. (3000mm Panels ONLY) * delete as required

• Fixings: 		M8 x 95 Cup square bolt with permacone nut

• Set posts: 	Set posts in holes 300 mm diameter x 800** mm deep, filled not less than half the depth with concrete, as clause 620.

• Maximum post centers: 	3010mm

• Bottom of fencing to be: 	approx. 50 mm above final ground level.

• Other requirements: 	PPC Colour Green RAL 6005. A full range of RAL Colours are available including marine grade and metallics.

** Depending on fence height

NOTES: 	All dimensions are nominal, for further information please contact Farm Relief Fencing. All information is correct at time of production. We reserve the right to alter specification without notice.